Android Usb Arduino Connection

Introduction

A simple Android application to communicate with Arduino MEGA 2560 and other Arduino Boards. All you need is a Micro USB OTG to USB Adapter.
This app will only send data to Arduino Board to change the intensity of the internal led present in Arduino MEGA 2560.
If the user wants to use external pin then they can change the pin number accordingly.

Requirements

Arduino IDE
- Android Studio (Optional)
- Android Phone ( Emulator will not work)
- Arduino Board ( Arduino MEGA 2560 preferred)
- Micro USB OTG to USB Adapter

Installation

1. Download the source code from the link given below.
2. Run the android source code which is pressent is Android -> Source Code folder in android studio and run it in your phone.
3. If you dont have Android Studio then go to Android -> APK folder. Apk of the source code is present in the folder. Send the apk to your phone and install the apk.
  1. If you are using Arduino Uno then take the apk from the Android-Uno-Usb folder.
  2. If you are using Arduino Mega then take the apk from the Android-Mega-Usb folder.
4. From the Arduino_Code folder take the Arduino code in Arduino Board Using Arduino IDE.
  1. If you are using Arduino Uno then take the code from the Android_Uno_Usb folder and take a LED whose positive side will be in pin 9 and the negative side will be in GND pin.
  2. If you are using Arduino Mega then take the code from the Android_Mega_Usb folder. You dont need extra LED as Mega boards come with internal LED and the pin of the LED is 13.
5. Connect the phone to arduino device using OTG cable and USB adapter of arduino.
6. Start the application.
7. Click on the enumerate button. It will ask for permission.

Output

After giving the application the required permission to use USB, the android device will be connected to arduino board. As the sliding bar is changed the intensity of the LED in the arduino board changes according to the sliding bar value.

Code Explanation

Android

The below code is an inner class of UsbController which is used to communicate between Android Device to Arduino Board.
private class UsbRunnable implements Runnable {
    private final UsbDevice mDevice;

    UsbRunnable(UsbDevice dev) {
        mDevice = dev;
    }

    @Override
    public void run() {	//here the main USB functionality is implemented
        UsbDeviceConnection conn = mUsbManager.openDevice(mDevice);
        if (!conn.claimInterface(mDevice.getInterface(1), true)) {
            return;
        }

        // Arduino USB serial converter setup

   conn.controlTransfer(0x21, 34, 0, 0, null, 0, 0);
        conn.controlTransfer(0x21, 32, 0, 0, new byte[] { (byte) 0x80,
                0x25, 0x00, 0x00, 0x00, 0x00, 0x08 }, 7, 0);

        UsbEndpoint epIN = null;
        UsbEndpoint epOUT = null;

        UsbInterface usbIf = mDevice.getInterface(1);
        for (int i = 0; i < usbIf.getEndpointCount(); i++) {
            if (usbIf.getEndpoint(i).getType() == UsbConstants.USB_ENDPOINT_XFER_BULK)	{
                if (usbIf.getEndpoint(i).getDirection() == UsbConstants.USB_DIR_IN)
                    epIN = usbIf.getEndpoint(i);
                else
                    epOUT = usbIf.getEndpoint(i);
            }
        }

        for (;;) {	// this is the main loop for transferring
            synchronized (sSendLock) {	//ok there should be a OUT queue, no guarantee that the byte is sent actually
                try {
                    sSendLock.wait();
                } catch (InterruptedException e) {
                    if (mStop) {
                        mConnectionHandler.onUsbStopped();
                        return;
                    }
                    e.printStackTrace();
                }
            }
            conn.bulkTransfer(epOUT, new byte[] { mData }, 1, 0);

            if (mStop) {
                mConnectionHandler.onUsbStopped();
                return;
            }
        }
    }
}

The first call sets the control line state, the second call sets the line encoding (9600, 8N1).
For communication, an additional thread is used to send data without blocking the Activity’s main UI thread. By notifying sSendLock of the UsbController the data will be transferred. After submission, the thread will go into “wait” again. This way, even if submission takes more time than expected, the Activity’s main thread will not be blocked and hence the app will not become unresponsive.

The below code is UsbController class is used to initialize the Controller so that Android-Arduino can be connected. It includes giving permission to the usb android.

class UsbController {
private final Context mApplicationContext;
private final UsbManager mUsbManager;
private final int VID;
private final int PID;
private static final String ACTION_USB_PERMISSION = "info.mayankag.usb_connection.USB";
UsbController(Activity parentActivity, int vid, int pid) {
  mApplicationContext = parentActivity.getApplicationContext();
  mUsbManager = (UsbManager) mApplicationContext.getSystemService(Context.USB_SERVICE);
  VID = vid;
  PID = pid;
  init();
}
private void init() {
  enumerate(new IPermissionListener() {
     @Override
     public void onPermissionDenied(UsbDevice d) {
        UsbManager usbman = (UsbManager)	mApplicationContext.getSystemService(Context.USB_SERVICE);
        PendingIntent pi = PendingIntent.getBroadcast(mApplicationContext, 0, new Intent(ACTION_USB_PERMISSION), 0);
        mApplicationContext.registerReceiver(mPermissionReceiver, new	IntentFilter(ACTION_USB_PERMISSION));
        usbman.requestPermission(d, pi);
     }
  });
}
private BroadcastReceiver mPermissionReceiver = new PermissionReceiver(
     new IPermissionListener() {
        @Override
        public void onPermissionDenied(UsbDevice d) {
        Log.d("USBController", ">< " + "Permission denied on " + d.getDeviceId()+ " ><");
        }
     });
private interface IPermissionListener {
  void onPermissionDenied(UsbDevice d);
}
}
Source Code is present at :
https://github.com/agarwalmayank32/Android-usb-Arduino-working-Code

Screenshots